## Slide 1: Wildfire Safety MCAR Presentation
Gaudenz Panholzer
Fire Chief
July 28, 2022

## Slide 2: Wildfire Preparedness
Home Hardening
Defensible Space

## Slide 3: Wildfire Preparedness
Home hardening
Defensible space

## Slide 4
Defensible Space
Harden Home

## Slide 5: Home Hardening
Use fire-resistive roofing and siding
Install a spark arrester on all chimneys
Cover all vent openings with 1/8th inch (max) mesh screen
Use fire-resistive materials for decks and fences
Install dual-pane windows with tempered glass
Use shutters or blinds in place of drapes
Box in eaves

## Slide 6: Home Hardening
Close in spaces under low decks
Remove vegetation and items that could catch fire from around and under decks, balconies and stairs
Remove dead or dry leaves and pine needles from your roof and rain gutters
Remove branches that hang over your roof and keep dead branches 10 feet away from your chimney
Make sure your address is visible from road

## Slide 7
Defensible Space
Immediate Zone: 0’-5’
Ember Resistant

## Slide 8: Immediate Zone Ember-Resistant Zone
Currently not required by law
Science has proven it to be the most important
Use hardscape like gravel, paver, concrete, etc.
Remove dead dying weeds
Only low-growing, nonwoody, maintained plants
Limit combustible items
Replace combustible fencing and gates

## Slide 9
Defensible Space
Intermediate Zone: 5’-30’
Lean, Clean, and Green

## Slide 10: Intermediate Zone Lean, Clean, & Green Zone
Extends out 30 feet from buildings, structures, decks
Remove all dead plants, grass and weeds (vegetation)
Remove dead or dry leaves and pine needles from your yard
Trim trees regularly to keep branches a minimum of 10 feet from other trees and 6 feet above the ground
Relocate wood piles to Extended Zone

## Slide 11
Defensible Space
Extended Zone: 30’-100’
Reduce Fuel

## Slide 12: Extended Zone Reduce Fuel Zone
Extends 30-100 feet from buildings, structures, decks
Mow annual grass down to a max height of 4 inches
Create horizontal space between shrubs and trees
Create vertical space between grass, shrubs and trees
Keep fallen leaves, needles, twigs, bark, cones, and small branches to a depth of 3 inches

## Slide 13
Defensible Space
All mitigation efforts stop at your property line

## Slide 14: Assembly Bill 38

## Slide 15: What is AB38?
Assembly Bill 38 established that, as of July 1, 2021, California Civil Code Section 1102.19 requires a seller of real property located in a High or Very High Fire Hazard Severity Zone to provide the buyer with documentation stating the property is in compliance with defensible space requirements.

## Slide 16: What is AB38?
The law allows, that if documentation demonstrating compliance cannot be obtained by the close of escrow, the seller and buyer can enter into a written agreement showing that the buyer agrees to obtain documentation of compliance within one year of the close of escrow.

## Slide 17: Fire Hazard Severity Zone (FHSZ)
California is divided into fire service areas:
  LRA – Local Responsibility Area
  SRA – State Responsibility Area
  FRA – Federal Responsibility Area
All of SRA has designated FHSZs
Many local jurisdictions have adopted FHSZs for LRA
FHSZ can be found at:
https://egis.fire.ca.gov/FHSZ/

## Slide 19: Defensible Space Regulations
  Public Resources Code Section 4291 requires maintaining a defensible space in SRA
    100 feet from each side and from the front and rear of the structure
    Not beyond the property line
  Many local agencies have adopted similar regulations in LRA

## Slide 20: Defensible Space Inspections
Many jurisdictions conduct annual Defensible Space Inspections
  Assist homeowners in keeping their properties safe

## Slide 21: Monterey Fire DSI Program
Public access to info at: www.monterey.org/fire
Legend

## Slide 22: Required Inspections
AB38 required inspections can be requested via fire agency having jurisdiction
  Go to: https://www.fire.ca.gov/dspace
  Click on link found on left side of page
Self-inspection survey on above web site

## Slide 24: DSI Request Form
Complete online form
You will receive a confirmation email
Appropriate local inspector will complete an inspection and provide you with results
Some agencies may charge a fee for this service

## Slide 25: Enforcement
No viable enforcement mechanism exists
May create liability risk for
  Seller / Buyer
  Agent / Broker (both sides)
May cause issues with financing and/or insurance
Compliance with Defensible Space requirements may result in insurance premium reduction

## Slide 26: Questions